## Slide 1
BUILDING AND DEVELOPMENT CONTROL
Willie Hannigan

## Slide 2
Building Control Regulations
New regulations cite the developments that require additional
documentation to be provided along with Commencement Notice.
The new certification is required for:
the design and construction of a new dwelling.
an extension to a dwelling involving a total floor area greater than 40 square metres.
Works to which Part III applies (require a Fire Safety Certificate).

## Slide 3
Building Control Regulations
A review of the application of the building control regulations in
relation to one off houses and domestic extensions is currently
ongoing.
Advisory rather than Mandatory
Broaden the pool of professionals who may sign certificates
Type of extensions that may be exempt

## Slide 4
Building Control Regulations
Commencement Notice to be accompanied by
such plans, calculations, specifications and particulars as are necessary to outline how the proposed works or building will comply with the requirements of the Second Schedule to the Building Regulations relevant to the works or building concerned and including –
general arrangement drawings including plans, sections
and elevations.
a schedule of such plans, calculations, specifications and
particulars as are currently designed or as are to be prepared
at a later date.
the completion of an online assessment, via the Building
Control Management System, of the proposed approach
to compliance with the requirements of the Second
Schedule to the Building Regulations.
the preliminary Inspection Plan prepared by the Assigned
Certifier.

## Slide 5
Building Control Regulations
Commencement Notice to be accompanied by
The following certificates and notices in the appropriate forms set out in the Second Schedule—
Certificate of Compliance (Design).
Notice of Assignment of Person to Inspect and Certify
Works (Assigned Certifier).
Certificate of Compliance (Undertaking by Assigned
Certifier).
Notice of Assignment of Builder.
Certificate of Compliance (Undertaking by Builder).
The appropriate fee.

## Slide 6
Building Control Regulations
Certificate of Compliance on Completion
Required for:
the design and construction of a new dwelling.
an extension to a dwelling involving a total floor area greater than 40 square metres.
Works to which Part III applies (require a Fire Safety Certificate).
A Certificate of Compliance on Completion shall be—
(a) in the form specified for that purpose in the Sixth Schedule of S.I. 9 OF 2014

## Slide 7
Building Control Regulations
Certificate of Compliance on Completion
(b) accompanied by such plans, calculations, specifications and
particulars as are necessary to outline how the works or
building as completed—
(i) differs from the plans, calculations, specifications and
particulars submitted with the Certificate of Compliance (Design)(to be
listed and included at the Annex to the Certificate of
Compliance on Completion), and
(ii) complies with the requirements of the Second Schedule
to the Building Regulations, and
(c) accompanied by the Inspection Plan as implemented by the
Assigned Certifier in accordance with the Code of Practice

## Slide 8
Building Control Regulations

## Slide 9
Taking in charge
Update on tic process:
Irish Water (IW) had, since it was established in January 2014, indicated that they would not be in a position to take private residential estates in charge until there was a protocol for doing so in place. As a result, no estates were taken in charge in 2014
In November 2014, The DoEC&LG issued a circular (5/2014) which provided clarity on how the tic process should proceed in conjunction with IW.
In February 2015. IW agreed a Memorandum of Understanding for the taking in charge of estates connected to the IW network

## Slide 10
Taking in charge
Update on tic process:
On the basis of this documents, Kildare County Council advertised the taking in charge of 38 private housing developments throughout the County in February 2015.
The Council has entered into a consultation process with Irish Water in relation to the taking in charge of the water services infrastructure elements of these developments.
It is hoped to bring most if not all of these estates to the relevant M.D. for taking in charge by the end of July 2015

## Slide 11
Taking in charge
Update on tic process:
In our recent discussions with IW, the issue of the taking in charge of developments that commenced since 1/1/2014 was raised.
They have indicated that for the time being, there will be no change in the current process and that KCC staff will still monitor water services infrastructure with a view to taking them in charge when completed to an acceptable standard.
Building and Development Control staff will advise Agents of any future documentary requirements that IW may have for taking estates in charge. These will also be addressed in a review of Kildare County Council's Taking in Charge Policy.